[PV204] Security Technologies
KeePassNFC applet
5. Improvement and Profiling

KeePassNFC applet functionality
The general functionality offered remains the same, with the addition of Master/User PIN management, and their requirement for verification to issue specific commands.
Also, the Password Key has now AES-256 format (AES-128 is not supported by KeePass[1]).
[1] https://keepass.info/help/base/security.html
Instructions and APDU formats changes
The applet now offer 3 different classes:
- [0x90]: commands always issuable
- [0xA0]: PIN verification/management commands
- [0xB0]: the old class, holds all previously present commands
Under [0x90] the instructions are:
- [0x74] - Get Version: the same function as before, copied under this different class
- [0x72] - Get Lock Reason: returns PIN trials available for both User and Master PINs. This is to be used mainly to understand if any command fail.
Under [0xA0] the instructions are:
- [0x80], [0x82] - Master and User PIN verification
- [0x81], [0x83] - Master and User PIN setting: both require the (old) Master PIN to be verified.
Under [0xB0] the old instructions are all present, even if [0x74] is deprecated and kept only for backward compatibility. All of them now issue proper SW errors. Besides, some of them received a change in APDU formats/behaviour:
- [0x76] - Write To Scratch: length checks are performed on the offset value provided, also in relation to the amount of data to write.
- [0x75] - Generate Card Key: input emptiness is checked, no flag is explicitly set about card cipher initialization.
- [0x70] - Get Card Public Key: the main change is that the Public Key modulus is always written to scratch before returning its value, to prevent improper data to be read.

Implementation of Best security practices
✅ Initialisation and Clearing of Sensitive data [❎]
After improvement, all sensitive data is cleared (zeroed) right when it is not needed anymore. Along with edits on [0x70], this improvement, prevents also the possibility to read decrypted database blocks.
✅ Use of exceptions [❎]
Exceptions are now catched, with cleaning of sensitive data done also in these situations. Moreover, proper SW error codes are issued.
✅ Initialisation of primitives and arrays [❎]
The primitives and byte arrays were initialised to NULL to remove garbage values.
✅ Fault induction checks [❎]
All sensitive checks were performed when absent (invalid CLA…), and redundancy was added to prevent the tampering with the instruction pointer of the smartcard.
✅/❎ Authorised Access [❎]
The applet didn’t provide any authorization and authentication to access the applet and to use/edit the current configuration of the card. A two-PIN based authentication (Master & User PINs) was implemented for JavaCard, with particular attention on the first setup and erasing of data when problems occur. Still, the PIN verification is done in plaintext.
However, considering the use-case for the applet, the usage of PIN mitigates the General Oracle attack and possible Padding Oracle/Side Channel attacks, by dropping unauthorized APDUs.

States
The implementation of PIN verification provides a first (partial) management of states. When states are not explicitly managed (such as for ciphers initialization), exceptions are raised effectively preventing some operations to be performed when particular objects are not ready to be used. Also the separation in 3 classes of commands helps in this. As it will be read in Future works, more consistent management can be done, even if after verification of the user with its PIN should prevent malicious APDUs to be sent trying to exploit the missing state management.
Right now, only two cases aren’t managed by clear exceptions: the setting of transaction and password keys. Indeed, if nothing has been written to the scratch area, those will be set to random values (sometimes returning errors because of zeroed initialization of the scratch area).

Profiling
Some profiling has been performed for all the commands (timings are in ms, average over 20 trials, smart-card NXP J2E 081). The results can be found in Appendix A.
About the B073 command (block decryption): a fully populated KeePass database can be long around 200 KiB, that corresponds to 1600 executions of given command. These result in a total execution time of around 150 seconds, or 2.5 minutes. This should be improved.
To use JCProfiler, keys setting and block decryption were chosen to test.
- For the Card Key generation, random operations are performed. These bring to inconsistent results (third breakpoint can last -13000 ms).
- All other operations require multiple APDUs requests for setup. In particular, the card public key must be used to encrypt some of the communications (password/transaction key), send it with WriteToScratch and then elaborate it. These cannot be simply performed by sending one static APDU.
  Even after trying to edit the PerfTests class to issue multiple APDUs for setup just once, the encryption could not be performed in the meanwhile.
- Even pre-preparing card status and inhibiting data cleanup on select doesn’t fix it.

Future work
This applet can be improved in several ways:
- HMAC encrypted communication
- Drop usage of 01/02 to show success/failure of commands, and just use SW codes
- Offer method to know the maximum amount of data that can be sent each time
- Support for long APDUs
- Support for encryption of database
- Support for ChaCha20/Twofish/other algorithms supported by KeePass or its plugins
- Manage states of the applet to prevent wrong commands to be called
- Setting initial Master/User PINs during installation with a payload
- DH-like key derivation instead of PIN/transaction key (with shared secret set during installation)
- Optimize for execution on real cards (currently, it can take several seconds or minutes to perform specific actions)
Also the repository can be improved:
- Leave a single build system, or correctly maintain/link both
- Provide multiple client implementations (different simulators/libraries)
- Run tests using different simulators and directly calling methods
- Add tests to cover all the applet code. Also, test and check coverage of clients.

Appendix A
Whole-command timings (over 20 measurements)
Header	Avg timing (ms)	Timing range (ms)	Notes
9072	7	7 - 8	(get lock reason/remaining PINs), direct read
9074	7	7 - 9	(get version), direct read
A080	37	37 - 39	(verify Master PIN)
A081	33	33 - 34	(set Master PIN)
A082	37	37 - 38	(verify User PIN)
A083	33	32 - 34	(set User PIN)
B070 / 010000	13	13 - 14	(get Card Key exponent) Supposed one execution every usage.
B070 / 020000	44	44 - 45	(get Card Key modulus - first part) Supposed one execution every usage.
B071	714	714 - 716	(set password key) Supposed one execution every long time.
B072	699	698 - 700	(set transaction key) Supposed one execution every usage.
B073 / P1!=80	96	95 - 97	(decrypt one block) Decrypting 128 bytes unique block.
B075	21660	5557 - 54592	(generate card key) Supposed one execution every long time.
B076	14	14 - 15	(write to scratch) Writing 16 bytes to scratch ~encrypted transaction key.
B076	18	18	(write to scratch) Writing 32 bytes to scratch ~encrypted password key.
B076	26	26 - 27	(write to scratch) Writing 64 bytes to scratch, more than needed by keys.